vGenInterface
vJoy and vXbox API
# General
vGenInterface is a collection of 3 APIs that can be used for writing a feeder for vXbox devices and for a mixture of vXbox/vJoy devices. It is also possible to use it for writing a vJoy-only feeder but it is currently recommended to use vJoyInterface API for that purpose.
vGenInterface offers three sets of interface functions:
1. Common API: Equally useful for vJoy and vXbox.
2. vJoy API: Backward Compatible with vJoyInterface. Also supports vXbox.
3. vXbox API: Tailored for vXbox feeders. Cannot be used for vJoy devices.
You can use a mixture of the above APIs if needed.
## Which API
Each API has it advantages and disadvantages. In addition, you can mix them without difficulty. You should first decide which kind of feeder you are writing:
#### vJoy Only:
If your feeder is designed to feed only vJoy devices, you should not use this API. Use vJoyInterface.dll instead.
#### Convert a Feeder:
Your feeder is written for vJoy devices and you use API file vJoyInterface.dll.
By linking to this (vGenInterface.dll) API you should get exactly the same results when target devices are vJoy devices.
If you want to add support for vXbox devices, it is recommended that you make at least the following minimal changes in your code:
1. Convert vXbox device index values to range 1001-1004
2. Report to the user the LED number of the vXbox device.

Additional changes you might introduce to improve your feeder:
1. Use vXbox virtual bus administrative functions:
  1. Call function isVBusExist() to verify that the system supports vXbox.
  2. Call function GetNumEmptyBusSlots() to see if you can add a new vXbox device.
2. If you want to support FFB add an FFB thread and poll Vibration status by repeatedly calling GetVibration() and passing vibration values to your hardware.
#### New Feeders:
If the new feeder is designed for only one of the target types, you can safely use either vXbox API or vJoyInterface.dll.
If the new feeder is designed to support both vJoy and vXbox, you should decide whether you want to take the agnostic approach or not.
Agnostic: Most operations will treat devices regardless to their type (vJoy/vXbox).
This approach simplifies the code but does not take advantage of the specifics of each type.
Example: you might need to check if button 10 exists before using it though it always exists for vXbox device.
Non-Agnostic: Most operations will treat devices according to their type (vJoy/vXbox).
This approach requires per-type coding making the code larger. However, it will enable the code to take advantage of the particular features of each type.
Example: You might take advantage of the large number of buttons in vJoy devices.
Note: It is OK to mix the approaches in your feeder code.
# vJoy API
This is an expansion of vJoyInterface API. It covers vJoy devices and vXbox devices.
The API treats vJoy devices exactly as vJoyInterface API.
The API treats vXbox devices in a similar way with a few exceptions:
- vXbox devices are identified by their ID. You will need to add 1000 (Decimal) to the original device ID hence for this API, the vXbox devices are in the range 1001-1004.
- No FFB support. Use specific vXbox FFB functions
- No LED-number support
- D-Pad: Supports only North, East, South and West.
- Axes (Thumb-stick): Lower resolution
# Common API
## Device Status
The following functions are used to change and to inquire the status of a virtual device.
Feeder life-cycle involve the acquisition of a virtual device, using it and finally relinquishing the device.
Only free devices can be acquired and by acquiring a device it becomes owned by the feeder. It is sometimes useful to know whether a device exists even if it is owned by another feeder.

### AcquireDev function
Acquire a Virtual Device
#### Syntax
DWORD AcquireDev(UINT DevId, DevType dType, HDEVICE * hDev);
#### Parameters
DevId
[in] ID of device to acquire
dType
[in] Type of device to acquire (vJoy or vXbox)
hDev
[out] Pointer that receives the handle to the acquired device
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If parameter dType is invalid, the return code is STATUS_INVALID_PARAMETER_2.
If the function fails and the type of the device is vXbox, see function PlugIn for return values.
If the function fails and the type of the device is vJoy, the return code is STATUS_UNSUCCESSFUL.

#### Remarks
Use this function to plug-in a new vXbox device or to acquire a new vJoy device. If the function succeeds it returns STATUS_SUCCESS and sets hDev to point to the handle to the device.
Once the device acquired, it is owned by the application and seen as existing or plugged-in by other applications.
To remove the device call function RelinquishDev(hDev) where the hDev parameter is the handle acquired by function AcquireDev().
Parameter DevId is the ID of the device to be acquired. If the device type is vJoy then it must be the ID of a free device, in the rage between 1 and 16. If the device type is vXbox then it must be the ID of an empty slot, in the rage between 1 and 4.
### RelinquishDev function
Relinquish a Virtual Device
#### Syntax
DWORD RelinquishDev(HDEVICE hDev);
#### Parameters
hDev
[in] The handle of the device to be relinquished.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If parameter hDev is an invalid handle, the return code is STATUS_INVALID_HANDLE.
If the function fails and the type of the device is vXbox, see function UnPlug for return values.
If the function fails and the type of the device is vJoy, the return code is STATUS_UNSUCCESSFUL.
#### Remarks
Use this function to unplug an owned vXbox device or to relinquish an owned vJoy device. You can only relinquish an owned device.
Once the function has successfully returned, the handle to the device cannot be used. It is recommended that you mark it as invalid by setting the handle variable to INVALID_DEV.

### isDevFree function
Test whether a Virtual Device is Free.
#### Syntax
DWORD isDevFree(UINT DevId, DevType dType, BOOL * Free);
#### Parameters
DevId
[in] ID of device to inquire.
dType
[in] Type (vJoy or vXbox) of device to inquire.
Free
[out] Result: TRUE if device is Free. FALSE otherwise.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer Free is invalid, the function returns STATUS_INVALID_PARAMETER_3.
Other return codes are possible.
#### Remarks
Use this function to checks whether a device is Free.
A Free device is not owned by any application.
Only Free devices can be acquired.
### isDevOwned function
Verify that a Virtual Device is owned.
#### Syntax
DWORD isDevOwned(UINT DevId, DevType dType, BOOL * Owned);
#### Parameters
DevId
[in] ID of device to inquire.
dType
[in] Type (vJoy or vXbox) of device to inquire.
Owned
[out] Result: TRUE if owned FALSE otherwise.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer Owned is invalid, the function returns STATUS_INVALID_PARAMETER_3.
Other return codes are possible.
#### Remarks
Use this function to checks if a device is owned by the current application. This function is useful to verify that a device is capable of receiving position data and if it is possible to relinquish the device.
An application can Relinquish (or unplug) only an owned device.
An application can feed with position data only an owned device.
Only an owned device has a valid handle.
### isDevExist function
Verify that a Virtual Device exists.
#### Syntax
DWORD isDevExist(UINT DevId, DevType dType, BOOL * Exist);
#### Parameters
DevId
[in] ID of device to inquire.
dType
[in] Type (vJoy or vXbox) of device to inquire.
Exist
[out] Result: TRUE if device exists FALSE otherwise.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer Owned is invalid, the function returns STATUS_INVALID_PARAMETER_3.
Other return codes are possible.
#### Remarks
Use this function to checks if a device exists.
An existing device is owned either by the current application or by another application.
There's no point in trying to acquire a device that 'Exists' – either it is already owned or it cannot be owned.
It is only possible to acquire a device that does not exist (or free).
## Device Information
The following functions are used to get information about an owned device.
Some information is related to the device capabilities such as the number of buttons, Hat switches and axes in the device.
Use the functions that inquire for the device capabilities to determine the existing controls while it is not an error to try to feed a non-existing control.
Some information is related to administrative data such as the device' type or the device' id.
Administrative data can be used if you want to mix function from all vGenInterface APIs.
You can obtain device ID and Type from a device Handle to be used by Backward Compatibility API or by the vXbox API.
You can obtain device Handle from device ID and Type, if the device was not created by the Common API.
You can also obtain the LED number of a vXbox device.

### isAxisExist function
For an owned Virtual Device, check whether a specific axis exists.
#### Syntax
DWORD isAxisExist(HDEVICE hDev, UINT nAxis, BOOL * Exist);
#### Parameters
hDev
[in] Handle of device to inquire.
nAxis
[in] Axis number (See remarks).
Exist
[out] Pointer to value: TRUE is axis exists, FALSE otherwise.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer Exist is invalid, the function returns STATUS_INVALID_PARAMETER_3.
If the device was removed (possibly by another application), the function returns STATUS_DEVICE_REMOVED.
#### Remarks
Use this function to check if a specific axis is configured in the specified virtual device.
May be used for owned devices only.
Useful mainly for vJoy devices because they are configurable. vXbox devices are not configurable so they will always report axes 1 to 6 as existing.
The axes are enumerated as follows:
#	vJoy	vXbox
1	X	X
2	Y	Y
3	Z	Trigger (R)
4	Rx	RX
5	Ry	RY
6	Rz	Trigger (L)
7	Slider 0	-
8	Slider 1	-

### GetDevButtonN function
For an owned Virtual Device, get the number of buttons.
#### Syntax
DWORD GetDevButtonN(HDEVICE hDev, UINT * nBtn);
#### Parameters
hDev
[in] Handle of device to inquire.
nBtn
[out] Pointer to the number of buttons.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer nBtn is invalid, the function returns STATUS_INVALID_PARAMETER_2.
If the device was removed (possibly by another application), the function returns STATUS_DEVICE_REMOVED.
#### Remarks
Use this function to get the number of buttons configured in the specified virtual device.
May be used for owned devices only.
Useful mainly for vJoy devices because they are configurable. vXbox devices are not configurable so they will always report 10 buttons.

### GetDevHatN function
For an owned Virtual Device, get the number of Hat Switches (a.k.a. POV) or D-Pads.
#### Syntax
DWORD DWORD GetDevHatN(HDEVICE hDev, UINT * nHat);
#### Parameters
hDev
[in] Handle of device to inquire.
nHat
[out] Pointer to the number of buttons.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer nHat is invalid, the function returns STATUS_INVALID_PARAMETER_2.
If the device was removed (possibly by another application), the function returns STATUS_DEVICE_REMOVED.
#### Remarks
Use this function to get the number of Hat switches or D-Pads configured in the specified virtual device.
May be used for owned devices only.
Useful mainly for vJoy devices because they are configurable. vXbox devices are not configurable so they will always report 1 D-Pad.
### GetDevHandle function
Retrieve the device handle from the devices' container.
#### Syntax
DWORD GetDevHandle(UINT DevId, DevType dType, HDEVICE * hDev);
#### Parameters
DevId
[in] ID of device to inquire.
dType
[in] Type (vJoy or vXbox) of device to inquire.
hDev
[out] Pointer to the handle corresponding to the indicated device.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle belongs to a device that is no longer owned, the return code is STATUS_DEVICE_REMOVED.
If pointer hDev is invalid, the function returns STATUS_INVALID_PARAMETER_3.
Other return codes are possible.
#### Remarks
#### This function is needed in cases where a device was Plugged-in or Acquired by another part of the API that does not return a device handle.
#### The function searches the device-container for a device that corresponds to the given ID/Type pair. If it finds it, the function verifies that the device is owned by the calling application and returns the handle if verified.
#### If a handle is found but it no longer represents an owned device, the function removes the entry from the device-container and returns STATUS_DEVICE_REMOVED.
### GetDevId function
Get the ID of an owned Virtual Device.
#### Syntax
DWORD GetDevId(HDEVICE hDev, UINT * dID);
#### Parameters
hDev
[in] Handle of device to inquire.
dID
[out] ID of a device.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer dID is invalid, the function returns STATUS_INVALID_PARAMETER_2.
If the device was removed (possibly by another application), the function returns STATUS_DEVICE_REMOVED.
#### Remarks
Use this function to retrieve the ID of an owned vXbox or vJoy device from its handle.
If the function is successful, dID will point to the ID of the virtual device.
#### Virtual Xbox devices (vXbox) have bus-wide unique IDs (Range 1-4). Do not confuse between vXbox IDs and Xbox LED Numbers.
### GetDevType function
Get the type of an owned Virtual Device.
#### Syntax
DWORD GetDevType(HDEVICE hDev, DevType * dType);
#### Parameters
hDev
[in] Handle of device to inquire.
dType
[out] Type of device (vJoy or vXbox).
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer pType is invalid, the function returns STATUS_INVALID_PARAMETER_2.
If the device was removed (possibly by another application), the function returns STATUS_DEVICE_REMOVED.
#### Remarks
Use this function to retrieve the type of an owned virtual device from its handle.
#### If the function is successful, dType will point to one of the predefined types (vJoy or vXbox).
### GetDevNumber function
Get the ID or LED Number of an owned Virtual Device.
#### Syntax
DWORD GetDevNumber(HDEVICE hDev, UINT * dNumber);
#### Parameters
hDev
[in] Handle of device to inquire.
dNumber
[out] LED Number of a vXbox device or the ID of a vJoy device.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If pointer pNumber is invalid, the function returns STATUS_INVALID_PARAMETER_2.
If the device was removed (possibly by another application), the function returns STATUS_DEVICE_REMOVED.
#### Remarks
Use this function to retrieve the LED Number of an owned vXbox device from its handle. For vJoy device the function retrieves the device ID.
If the function is successful, dNumber will point to the LED Number of the vXbox device or to the ID of the vJoy device.
#### Every plugged-in Xbox device (Physical or virtual) receives from the system a unique LED number. Physical devices Illuminate a quarter of a circle LED that indicates it's number. In addition virtual Xbox devices (vXbox), have bus-wide unique IDs (Range 1-4). Do not confuse between vXbox IDs and Xbox LED Numbers.
## Device Feeding
The following functions are used to feed the virtual device with position data. Position data is the exact position of each vJoy axes, vXbox thumb-stick, vXbox trigger, button and Hat Switch.
Hat switches as sometimes referred to as POVs. The vXbox equivalent is D-Pad.
The axes, thumb-stick and triggers have specific names. However, the common API enumerates them as follows:
	1	2	3	4	5	6	7	8
vJoy	X	Y	Z	Rx	Ry	Rz	Slider 0	Slider 1
vXbox	Left-X	Left-Y	Right-Trigger	Right-X	Right-Y	Left-Trigger	-	-

The axes, thumb-stick and triggers have different ranges. However, the common API feeds them with position values of 0.00 to 100.00. The actual positions are mapped as follows:
Value	vJoy Axes	vXbox
		Axes	Triggers
0	0	-32768	0
50	16384	0	127
100	32768	32767	255

A vJoy device may contain up to four Hat switch devices enumerated 1 to 4. The Hat switches may be continuous or discrete. Continuous Hat switches position ranges from 0° to 359.99°. Discrete Hat switches may be in one of 4 positions: 0° (North), 90° (East), 180° (South), 270° (West). Hat switches (of both types) may also be in Neutral position.
A vXbox device has one D-Pad which is referred to as Hat switch number 1. It may be in the Neutral position or in one of the eight positions as described in the following table:
Value	Position		Applies to:
			Continuous (vJoy)	Discrete (vJoy)	D-Pad
0%	North	0°	✅	✅	✅
12.5%	North-East	45°	✅		✅
25%	East	90°	✅	✅	✅
37.5%	South-East	135°	✅		✅
50%	South	180°	✅	✅	✅
62.5%	South-West	225°	✅		✅
75%	West	270°	✅	✅	✅
87.5%	North-West	315°	✅		✅
99%	Almost North	356.4°	✅

Note the the common API feeds the Hat with position values of 0.00 to 99.99.

A vJoy device may contain up to 128 buttons. However, the Common API supports only the first 32 buttons. The buttons are simply enumerated 1 to 32.
A vXbox device always contains ten buttons. Each button has a unique function. However, the common API refers to them by a serial number as follows:
1	2	3	4	5	6	7	8	9	10
A	B	X	Y	Left- Shoulder	Right- Shoulder	Back	Start	Left-thumb	Right-thumb

### SetDevAxis function
Set position of virtual device axis or trigger.
#### Syntax
DWORD SetDevAxis(HDEVICE hDev, UINT Axis, FLOAT Value);
#### Parameters
hDev
[in] Handle of device to feed.
Axis
[in] Axis or trigger to change.
Value
#### [in] Position of axis in the range 0 to 100
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set an axis or trigger control of the specified device to the required position.
Meaning of Axis parameter:
	1	2	3	4	5	6	7	8
vJoy	X	Y	Z	Rx	Ry	Rz	Slider 0	Slider 1
vXbox	Left-X	Left-Y	Right-Trigger	Right-X	Right-Y	Left-Trigger	-	-

Parameter Value ranges between 0 and 100 and is passed as a FLOAT to enable high precision. The value is mapped to an internal value based on the specifics of the target axis:
Value	vJoy Axes	vXbox
		Axes	Triggers
0	0	-32768	0
50	16384	0	127
100	32768	32767	255

### SetDevPov function
Set position of virtual Pov (Hat Switch) or D-Pad.
#### Syntax
DWORD SetDevPov(HDEVICE hDev, UINT nPov, FLOAT Value);
#### Parameters
hDev
[in] Handle of device to feed.
nPov
[in] Hat switch (a.k.a. POV) or D-Pad to control
Value
#### [in] Position of switch in degrees (range 0 to 359.99)
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set a POV Hat switch or D-Pad control of the specified device to the required position.
vJoy supports up to four POV hat switches that can be of two types: Continuous or Discrete.
vXbox supports exactly one D-Pad which supports eight directions.
These controls can also be in neutral state.
POV hat Switches are accessed by their serial number (1-4). The D-Pad is considered as POV hat Switch number 1.
The value passed to a POV hat Switch/D-pad control ranges between 0 and 359.99. Value -1 corresponds to the neutral state.
Example Values:
Value	Position		Applies to:
			Continuous (vJoy)	Discrete (vJoy)	D-Pad
0.00	North	0°	✅	✅	✅
45.00	North-East	45°	✅		✅
90.00	East	90°	✅	✅	✅
135.00	South-East	135°	✅		✅
180.00	South	180°	✅	✅	✅
225.00	South-West	225°	✅		✅
270.00	West	270°	✅	✅	✅
315.00	North-West	315°	✅		✅
356.33	Almost North	356.33°	✅
-1	Neutral	-	✅	✅	✅

### SetDevButton function
Press/Release one or more virtual device buttons.
#### Syntax
DWORD SetDevButton(HDEVICE hDev, UINT Button, BOOL Press);
#### Parameters
hDev
[in] Handle of device to feed.
Button
[in] Button(s) to Press or Release
Press
#### [in] Press or Release button
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If the function fails because the handle is invalid or if the handle belongs to a device that is no longer owned, the return code is STATUS_INVALID_HANDLE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to Press or Release one or more buttons of the specified device.
If you want to Press the buttons, set parameter Press to TRUE.
If you want to Release the buttons, set parameter Press to FALSE.
Specify the button to Press or Release by setting the correct value in parameter Button.
The vXbox buttons are enumerated as followed:
1	2	3	4	5	6	7	8	9	10
A	B	X	Y	Left- Shoulder	Right- Shoulder	Back	Start	Left-thumb	Right-thumb

# vXbox API
## Virtual vXbox bus information

The following functions return information about the Virtual USB bus that the xXbox devices may be connected to. This but presents 4 virtual slots to which vXbox devices may be plugged-in.
An Empty Slot is a slot into which it is possible to plug-in a new vXbox device.
### isVBusExist function
Tests that Virtual USB bus exists.
#### Syntax
DWORD isVBusExist(void);
#### Parameters
None.

#### Return Value
If the function finds a valid virtual bus installed on the computer, the return code is STATUS_SUCCESS.
If there is no such bus, the function returns STATUS_NO_SUCH_DEVICE.
#### Remarks
Always use this function before any other vXbox related operation.
If the Virtual USB bus is absent then there's no point to continue.
### GetNumEmptySlots function
Tests that Virtual USB bus exists.
#### Syntax
DWORD GetNumEmptySlots(UCHAR * nSlots);
#### Parameters
nSlots
[out] Pointer that receives the number of empty vXbox slots. Use this number to determine how many vXbox devices can still be plugged-in.
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
#### Remarks
Use this function if you want to test how many slots are available.
The number of available slots is the number of possible slots (4) minus the number of vXbox devices plugged-in by all feeders.
## Device Status
The following functions are used to change and to inquire the status of a vXbox device.
An application may plug-in a vXbox device into an empty slot (or free slot). Once the devices is plugged in, the slot is no longer empty and this device is considered as plugged-in.
The plugged-in device is said to be owned by the application that plugged it in.
The virtual devices are enumerated between 1 to 4. The application can access every device (or slot) by its UserIndex. However, the UserIndex of a device is not recognized by the system. The system recognizes the device by its LED number.
When the application no longer needs an owned device, it should unplug it. By this the corresponding bus-slot becomes empty.
Only an application that owns a vXbox device can unplug it. In the rare cases that an application has crashed and its devices were not unplugged you may use force unplug. Use this option with extreme caution.

### PlugIn function
Plugged-in a vXbox controller in the specified slot.
#### Syntax
DWORD PlugIn(UINT UserIndex);
#### Parameters
UserIndex
[in] Index of the target slot.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the virtual USB bus is missing, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If device already plugged-in in the specified socket, the function returns STATUS_DEVICE_ALREADY_ATTACHED.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device failed to start after it has been inserted, the function will unplug it and return STATUS_DEVICE_NOT_READY.
If the DLL fails to create a handle for this device, the function will unplug the device and return STATUS_INVALID_HANDLE.
#### Remarks
Use this function to plug-in a vBox device in the user-specifies slot. Indices are bus-wide unique and range between 1 and 4.
Do not confuse UserIndex (which is a virtual bus internal index) with the system-wide recognized LED number (or index).
If a device is plugged-in (or exists) in a specified slot the function will fail.
After the function returns successfully, the device is Plugged-in, Owned by the current feeder and its handle is valid and may be obtained by calling function GetDevHandle.
To remove the device call function UnPlug or UnPlugForce.

### PlugInNext function
Plugged-in a vXbox controller in the next free slot.
#### Syntax
DWORD PlugInNext(UINT * UserIndex);
#### Parameters
UserIndex
[out] Pointer that receives the device User Index.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the virtual USB bus is missing, the function returns STATUS_NO_SUCH_DEVICE.
If device cannot be plugged-in because all sockets already in use, the function returns STATUS_DEVICE_ALREADY_ATTACHED.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device failed to start after it has been inserted, the function will unplug it and return STATUS_DEVICE_NOT_READY.
If the DLL fails to create a handle for this device, the function will unplug the device and return STATUS_INVALID_HANDLE.
#### Remarks
Use this function to plug-in a vBox device in any available slot. If successful, the selected slot index is pointed by UserIndex. Indices are bus-wide unique and range between 1 and 4.
Do not confuse UserIndex (which is a virtual bus internal index) with the system-wide recognized LED number (or index).
If there are no available slots (4 devices are already plugged-in) the function will fail.
After the function returns successfully, the device is Plugged-in, Owned by the current feeder and its handle is valid and may be obtained by calling function GetDevHandle.
To remove the device call function UnPlug or UnPlugForce
### UnPlug function
Unplug an owned controller from the specified slot.
#### Syntax
DWORD UnPlug(UINT UserIndex);
#### Parameters
UserIndex
[in] Index of the device to unplug
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the virtual USB bus is missing, the function returns STATUS_NO_SUCH_DEVICE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If specified device does not exist, the function returns STATUS_DEVICE_DOES_NOT_EXIST.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If Device failed to unload after a long wait, the function returns STATUS_TIMEOUT.
#### Remarks
Use this function unplug (Remove) devices from the specified slot. Indices are bus-wide unique and range between 1 and 4.
Do not confuse UserIndex (which is a virtual bus internal index) with the system-wide recognized LED number (or index).
The feeder can unplug only devices that it owns. The feeder owns only devices it has plugged-in. It does not own devices plugged-in by another feeder.
Only plugged-in device can be unplugged.
### UnPlugForce function
Unplug a controller from the specified slot even if not owned.
#### Syntax
DWORD UnPlugForce(UINT UserIndex);
#### Parameters
UserIndex
[in] Index of the device to unplug
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the virtual USB bus is missing, the function returns STATUS_NO_SUCH_DEVICE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If specified device does not exist, the function returns STATUS_DEVICE_DOES_NOT_EXIST.
If Device failed to unload after a long wait, the function returns STATUS_TIMEOUT.
#### Remarks
Warning: This function will remove any device including devices that are owned by other feeders.
Use this function unplug (Remove) devices from the specified slot. Indices are bus-wide unique and range between 1 and 4.
Do not confuse UserIndex (which is a virtual bus internal index) with the system-wide recognized LED number (or index).
Only plugged-in device can be unplugged.
### isControllerPluggedIn function
Tests that a vXbox controller is plugged-in in the specified slot.
#### Syntax
DWORD isControllerPluggedIn(UINT UserIndex, PBOOL Exist);
#### Parameters
UserIndex
[in] Index of the slot to test.
Exist
[out] Pointer that receives the Boolean value. Valid only when function returns STATUS_SUCCESS.
TRUE if a vBox device is plugged-in in the specifies slot.
FALSE if specifies slot is empty.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the virtual USB bus is missing, the function returns STATUS_NO_SUCH_DEVICE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If UserIndex is out of range , the function returns STATUS_INVALID_PARAMETER.
#### Remarks
Use this function to test existence of a vBox device in the user-specifies slot. Indices are bus-wide unique and range between 1 and 4.
Do not confuse UserIndex (which is a virtual bus internal index) with the system-wide recognized LED number (or index).
If a device is plugged-in (or exists) in a specified slot it means that another device cannot be plugged in into this slot.
The feeder can control only devices that it owns. The feeder owns only devices it has plugged-in. It does not own devices plugged-in by another feeder.
### isControllerOwned function
Tests that a vXbox controller is plugged-in in the specified slot.
#### Syntax
DWORD isControllerOwned(UINT UserIndex, PBOOL Owned);
#### Parameters
UserIndex
[in] Index of the slot to test.
Owned
[out] Pointer that receives the Boolean value. Valid only when function returns STATUS_SUCCESS.
TRUE if a vBox device in the specifies slot is owned by the current feeder.
FALSE if a vBox device in the specifies slot is not owned by the current feeder.
#### Return Value
If the function successful, the return code is STATUS_SUCCESS.
If the virtual USB bus is missing, the function returns STATUS_NO_SUCH_DEVICE.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If UserIndex is out of range , the function returns STATUS_INVALID_PARAMETER.
#### Remarks
Use this function to test if the vBox device in the user-specifies slot is owned by the current feeder. Indices are bus-wide unique and range between 1 and 4.
Do not confuse UserIndex (which is a virtual bus internal index) with the system-wide recognized LED number (or index).
The feeder can control only devices that it owns. The feeder owns only devices it has plugged-in. It does not own devices plugged-in by another feeder.
Only plugged-in device can be owned.
### GetLedNumber function
Get the LED Number associated with a vXbox device..
#### Syntax
DWORD GetLedNumber(UINT UserIndex, PBYTE pLed);
#### Parameters
UserIndex
[in] Index of the device
pLed
[out] Pointer that receives the LED Number associated with the current device.
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If the DLL fails to create a handle for this device, the function will unplug the device and return STATUS_INVALID_HANDLE.
If pointer pLed is invalid, the function returns STATUS_INVALID_PARAMETER_2.
#### Remarks
Use this function to retrieve the LED number (a.k.a. LED Index) associated with the current device. This number represents the illuminated quarter-circle that indicates the Controller number.
The LED Number is not related to the User Index of the vXbox device.
## Device Position Control
The following functions change the position of the vXbox device controls.
They change the position of the Axes, Trigger buttons, buttons and D-Pad.
The functions that control the Axes and the Trigger buttons set each control individually. The functions that control the buttons and the D-Pad may set/reset a number of controls simultaneously.
There are also functions that reset a device to its neutral position:
- Axes are centered.
- Trigger buttons not pressed
- Buttons released
- D-Pad in neutral position
### SetAxisLx function
Set Left Stick X-Axis to specified value
#### Syntax
DWORD SetAxisLx(UINT UserIndex, SHORT Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Axis value (Range: -32768 to 32767 )

#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If Value is out of range, the function returns STATUS_INVALID_PARAMETER_2.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set the position of the X-Axis in the Left-thumb stick of the specified device.
The valid range is -32768 to 32767. Center value is 0.
### SetAxisLy function
Set Left Stick Y-Axis to specified value
#### Syntax
DWORD SetAxisLy(UINT UserIndex, SHORT Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Axis value (Range: -32768 to 32767 )

#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If Value is out of range, the function returns STATUS_INVALID_PARAMETER_2.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set the position of the Y-Axis in the Left-thumb stick of the specified device.
The valid range is -32768 to 32767. Center value is 0.
### SetAxisRx function
Set Right Stick X-Axis to specified value
#### Syntax
DWORD SetAxisRx(UINT UserIndex, SHORT Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Axis value (Range: -32768 to 32767 )

#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If Value is out of range, the function returns STATUS_INVALID_PARAMETER_2.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set the position of the X-Axis in the Right-thumb stick of the specified device.
The valid range is -32768 to 32767. Center value is 0.
### SetAxisRy function
Set Right Stick Y-Axis to specified value
#### Syntax
DWORD SetAxisRy(UINT UserIndex, SHORT Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Axis value (Range: -32768 to 32767 )

#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If Value is out of range, the function returns STATUS_INVALID_PARAMETER_2.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set the position of the Y-Axis in the Right-thumb stick of the specified device.
The valid range is -32768 to 32767. Center value is 0.
### SetTriggerL function
Set Left Trigger to specified value
#### Syntax
DWORD SetTriggerL(UINT UserIndex, BYTE Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Trigger value (Range: 0-255)

#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If Value is out of range, the function returns STATUS_INVALID_PARAMETER_2.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set the position of the Left Trigger of the specified device.
The valid range is 0 to 255.
### SetTriggerR function
Set Right Trigger to specified value
#### Syntax
DWORD SetTriggerR(UINT UserIndex, BYTE Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Trigger value (Range: 0-255)

#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If Value is out of range, the function returns STATUS_INVALID_PARAMETER_2.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to set the position of the Right Trigger of the specified device.
The valid range is 0 to 255.
### SetButton function
Press/Release one or more vBox device buttons.
#### Syntax
DWORD SetButton(UINT UserIndex, WORD Button, BOOL Press);
#### Parameters
UserIndex
[in] Index of the device
Button
[in] Button(s) to Press or Release
Press
#### [in] Press or Release button
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to Press or Release one or more buttons of the specified device.
If you want to Press the buttons, set parameter Press to TRUE.
If you want to Release the buttons, set parameter Press to FALSE.
Specify the button(s) to Press or Release by setting the correct value in parameter Button. You may OR two or more button values.
Button values are defined in header file Xinput.h (part of the WDK). The available values are:
XINPUT_GAMEPAD_START	0x0010
XINPUT_GAMEPAD_BACK	0x0020
XINPUT_GAMEPAD_LEFT_THUMB	0x0040
XINPUT_GAMEPAD_RIGHT_THUMB	0x0080
XINPUT_GAMEPAD_LEFT_SHOULDER	0x0100
XINPUT_GAMEPAD_RIGHT_SHOULDER	0x0200
XINPUT_GAMEPAD_A	0x1000
XINPUT_GAMEPAD_B	0x2000
XINPUT_GAMEPAD_X	0x4000
XINPUT_GAMEPAD_Y	0x8000

### SetDpad function
Press one or more vBox device D-Pad Directions.
#### Syntax
DWORD SetDpad(UINT UserIndex, UCHAR Value);
#### Parameters
UserIndex
[in] Index of the device
Value
[in] Direction(s) to press
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to Press one or more D-Pad directions of the specified device.
Specify the direction(s) to Press by setting the correct value in parameter Value. You may OR two or more direction values.
Every call to this function replaces the previous D-Pad state.
Use value=0 to depress all directions.
Direction values are defined in header file Xinput.h (part of the WDK). The available values are:
XINPUT_GAMEPAD_DPAD_UP	0x0001
XINPUT_GAMEPAD_DPAD_DOWN	0x0002
XINPUT_GAMEPAD_DPAD_LEFT	0x0004
XINPUT_GAMEPAD_DPAD_RIGHT	0x0008

### ResetController function
Reset all vBox device controls.
#### Syntax
DWORD ResetController(UINT UserIndex);
#### Parameters
UserIndex
[in] Index of the device
#### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to reset all controls of the specified device.
If successful, the device controls are reset to the following values:
- Axes: Centered (Value=0)
- Triggers: Minimum (Value=0)
- Buttons: Released
- D-Pad: Neutral (centered)

### ResetAllControllers function
Reset controls on all all vBox devices.
##### Syntax
DWORD ResetAllControllers(void);
#### Parameters
None
##### Return Value
If the function succeeds, the return code is STATUS_SUCCESS.
If there is no virtual USB bus, the function returns STATUS_NO_SUCH_DEVICE.
If UserIndex is out of range, the function returns STATUS_INVALID_PARAMETER.
If the API fails to get the information from the virtual USB bus, the function returns STATUS_IO_DEVICE_ERROR.
If device does not exist, the function will return STATUS_DEVICE_DOES_NOT_EXIST.
If device failed to start after it has been inserted, the function will return STATUS_DEVICE_NOT_READY.
If specified device is not owned by the current feeder, the function returns STATUS_RESOURCE_NOT_OWNED.
If the current position pf the device cannot be obtained, the function returns STATUS_MEMORY_NOT_ALLOCATED.
#### Remarks
Use this function to reset all controls of all vXbox device.
If successful, the device controls are reset to the following values:
- Axes: Centered (Value=0)
- Triggers: Minimum (Value=0)
- Buttons: Released
- D-Pad: Neutral (centered)