vXbox API
C-Language

# Interface Functions
The following functions are used to Plug-in/Unplug and communicate with vXbox devices installed on ScpVBus.
## Status Functions
BOOL	isVBusExists(void)
Description:
Use this function to verify that the bus exists. You can plug-in vXbox devices only if the bus exists.
Returns:
TRUE if ScpVBus exists. Otherwise FALSE.

BOOL	GetNumEmptyBusSlots(UCHAR * nSlots)
Description:
Virtual bus ScpVBus has 4 slots for vXbox devices. Use this function to query the number of slots that it is possible to plug-in new device into.
Parameter:
nSlots	Pointer to number of empty slots. Range: 0 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	isControllerExists(UINT UserIndex)
Description:
Check if a specified slot is occupied by a vXbox device (Controller).
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if controller plugged-in. Otherwise FALSE.

BOOL	isControllerOwned(UINT UserIndex)
Description:
Check if a vXbox device (Controller) is owned by the calling application.
Owned means Exists (=was plugged in) and the ID of the plugging process is the same as that of the current process.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if controller owned by application. Otherwise FALSE.

## Plugged-in/Unplug Functions
BOOL	PlugIn(UINT UserIndex)
Description:
Plug-in a vXbox device in a specified slot.
The operation will fail unless the bus exists and the slot is free.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	UnPlug(UINT UserIndex)
Description:
Unplug a vXbox device from a specified slot.
The operation will fail unless the bus exists and the slot is occupied by an owned device.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	UnPlugForce(UINT UserIndex)
Description:
Unplug a vXbox device from a specified slot.
The operation will fail unless the bus exists and the slot is occupied by a device.
Warning: This function may remove a vXbox device that is owned by another process.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

## Data Feeding Functions
The following functions are used for feeding the vXbox device with data such as button press/release, axis position or trigger pressure.
BOOL	SetBtnA(UINT UserIndex, BOOL Press)
Description:
Button A Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnB(UINT UserIndex, BOOL Press)
Description:
Button B Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnX(UINT UserIndex, BOOL Press)
Description:
Button X Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnY(UINT UserIndex, BOOL Press)
Description:
Button Y Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnStart(UINT UserIndex, BOOL Press)
Description:
Button Start Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnBack(UINT UserIndex, BOOL Press)
Description:
Button Back Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnLT(UINT UserIndex, BOOL Press)
Description:
Left Stick (Left Thumb) Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnRT(UINT UserIndex, BOOL Press)
Description:
Right Stick (Right Thumb) Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnLB(UINT UserIndex, BOOL Press)
Description:
Left Bumper Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetBtnRB(UINT UserIndex, BOOL Press)
Description:
Right Bumper Pressed/Released
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Press	TRUE (Button Pressed) or FALSE (Button Released)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetTriggerL(UINT UserIndex, BYTE Value)
Description:
Set Left Trigger Value
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Value	Press trigger value. Range: 0 to 255
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetTriggerR(UINT UserIndex, BYTE Value)
Description:
Set Right Trigger Value
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Value	Press trigger value. Range: 0 to 255
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetAxisX(UINT UserIndex, SHORT Value)
Description:
Set Value of the left thumb stick X position
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Value	Stick Position. Range: -32768 to 32767 (Neutral point is 0)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetAxisY(UINT UserIndex, SHORT Value)
Description:
Set Value of the left thumb stick Y position
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Value	Stick Position. Range: -32768 to 32767 (Neutral point is 0)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetAxisRx(UINT UserIndex, SHORT Value)
Description:
Set Value of the Right thumb stick X position
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Value	Stick Position. Range: -32768 to 32767 (Neutral point is 0)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetAxisRy(UINT UserIndex, SHORT Value)
Description:
Set Value of the Right thumb stick Y position
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Value	Stick Position. Range: -32768 to 32767 (Neutral point is 0)
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetDpadUp(UINT UserIndex)
Description:
D-Pad pressed UP.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetDpadDown(UINT UserIndex)
Description:
D-Pad pressed DOWN.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetDpadLeft(UINT UserIndex)
Description:
D-Pad pressed LEFT.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetDpadRight(UINT UserIndex)
Description:
D-Pad pressed RIGHT.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	SetDpadOff(UINT UserIndex)
Description:
D-Pad is released.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
Returns:
TRUE if function succeeded. Otherwise FALSE.

## Feedback Functions
The following functions are used for getting feedback from the vXbox device. These functions poll the device.

BOOL	GetLedNumber(UINT UserIndex, PBYTE pLed)
Description:
Get the serial number of the LED that should light on the Xbox controller. Note that this is not the slot number. Rather, it is a arbitrary number in the range 1 to 4 that the system attach to the device.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
pLed	The serial number of the LED. Range: 1-4
Returns:
TRUE if function succeeded. Otherwise FALSE.

BOOL	GetVibration(UINT UserIndex, PXINPUT_VIBRATION pVib)
Description:
Get the vibration intensity of each of the two vibrating motors.
Parameter:
UserIndex	Slot Index. Range: 1 to 4
pVib	Structure holding the output data. (See description)
Returns:
TRUE if function succeeded. Otherwise FALSE.